1974 Porsche 914-6 2.2 liter Race Car:  Very fast. Very light. Drives, handles and shifts like a shifter cart, only bigger! Everything that can be done to the car, and still be safe, has been done! Current PCA and Vintage / VSCR log books. Professionally built and maintained by Bob Viau and his team at Auto Edge for the last 10 years.  PCA GT5R or S class. PCA, NASA, SCCA, POC and Vintage legal. Current PCA inspection, (4/20/07).

Very reliable. Recent rebuild on engine and transmission with test hours only. New suspension. 15 podium finishes in last 20 starts.

Engine: (Andail / Porsche Motorsports Specs. Recent rebuild with test hours only)

- 2.2  liter twin plug six cylinder

- Webber 40 carburetors

- Induction Research flowed 2.4 liter Porsche twin plug heads

- Extensive machining to case and crank

- Pauter Rods, 70 mm stroke

- J&E Pistons custom coated 81mm. 9.8/1 compression

- Custom Web Cams, 104/102 grind

- Titanium retainers with Jerry Woods high tension valve springs

- Tuned length headers with EGT probes, Jet Hot ceramic coated

- Sport tuned stainless steel muffler

- Peterson 16qt front mount tank with heater, front cooler and Accusump pre-lube

- All Aeroquip hoses with Earls fittings

- Electromotive crank fire – waste spark ignition

- Turbo valve covers

- New wiring with blade style fuses, all labeled

- Front mounted case breather system with catch can

- Facet electronic fuel pump with micron filters

Suspension: (New suspension with test hours only)

- Front: Bilstein RSR 220/100 valveing Mono ball mounting

- Koni double adjustable rear.

- Hypercoil springs

- SMR Bump steer kit

- Adjustable front sway bar with mono ball links

- All mono ball or Delrin bushings

Brakes: (This car has way more brakes than it needs!)

- 1986 930 front calipers and rotors on the front and rear,

- Cross drilled rotors

- Stainless steel lines

- Adjustable proportioning valve

Sequential Transmission:

- Porsche case / bell housing containing a Hewland Webster Mark 9 with Mark 5 gears

- PBS sequential shift linkage

- New dog rings

- Ratios: Ring and Pinion: 8/31 1st 12/31 2nd 17/29 3rd 16/23 4th 19/24 5th 24/27

- Quafe limited slip differential

Tub / Chassis: (Very stiff chassis! Absolutely no rust!)

- Porsche tub with 914 GT fiberglass body panels

- All fiberglass body except door skins

- Full custom roll cage welded to the chassis with all suspension points tied in

- NASCAR style intrusion bars on the driver side.

- Factory rear suspension reinforcement plates welded in with additional custom reinforcement

- Reinforced rockers

- Floor pans and rockers replaced last year with NOS parts.

- Paint is a 7 ½ out of 10, Rino-tape on the front end. Some race rash on Rino-Tape in the front. Small dent on the top of the windshield hoop otherwise in great shape!

- Custom gages. Tachometer, Oil Pressure, Oil Temp, EGT gages for each cylinder

- AIM Data Acquisition System

- Custom center panel with EGT switches, Ignition, Accusump activator, Cool Suit air and water regulators, Radio push to talk.

- Rebuilt pedal cluster with bronze bushings, (stock was prone to fail)

- 914 M471 GT Engine cover, (for better cooling)

Safety:

- Autoshield aluminum seat bolted to the floor and the roll cage

- Lexan windshield with anti scratch coating.

- Large convex rear view mirror

- Areo convex side mirrors

- SPA fire system with jets on the fuel cell, engine and driver. Activation switches on the outside and inside of the car

- Battery cut off switch

- New Simpson 6 point harnesses

- Cool Suit air and water system, (Cool Shirts not included)

- Wired for radios, (radios not included)

- Removable Sparco steering wheel with quick release

Spares included:

- 3 Front air dams

- 2 Sets of 8 x 15 Fuch wheels

- 8 New Hoosier racing slicks

- 6 Fuel cans

- Custom fuel funnel

- Set of new brake pads

- Several fuel and oil filters

- Some other little parts, (shift cable, clutch cable, bumper, engine cover, engine shroud)

This car cost $125,000 to build. Asking $50,000 OBO.  Contact danmuldowney@comcast.net or (952) 941-2039